# Cooper Home Inspections

Building Inspection Report

1234 Main St

Inspection Date:

5/5/07

Prepared For:

John Smith

Prepared By:

Cooper Home Inspections

15915 SE Monner

Portland OR 97236

503-807-8199

503-658-7918 Fax

Report Number:

1234

Inspector:

Steve Cooper

CCB #50406  OCHI #258

© 2007 Cooper Home Inspections

# Report Overview

## THE HOUSE IN PERSPECTIVE

## CONVENTIONS USED IN THIS REPORT

For your convenience, the following conventions have been used in this report.

- Major Concern:  denotes a major improvement recommendation that is uncommon for a home of this age or location.

- Safety Issue:  denotes an observation or recommendation that is considered an immediate safety concern.

- Improve:  denotes improvements that should be anticipated over the short term.

- Monitor:  denotes an area where further investigation and/or monitoring is needed.  Repairs may be necessary.   During the inspection, there was insufficient information.  Improvements cannot be determined until further investigation or observations are made.

Please note that those observations listed under “Discretionary Improvements” are not essential repairs, but represent logical long-term improvements.

NOTE: For the purpose of this report, it is assumed that the house faces north.

## IMPROVEMENT RECOMMENDATION HIGHLIGHTS

The following is a synopsis of the potentially significant improvements that should be budgeted for over the short term.  Other significant improvements, outside the scope of this inspection, may also be necessary.  Please refer to the body of this report for further details on these and other recommendations.

## THE SCOPE OF THE INSPECTION

All components designated for inspection in the ASHI( Standards of Practice are inspected, except as may be noted in the “Limitations of Inspection” sections within this report.

This inspection is visual only.  A representative sample of building components are viewed in areas that are accessible at the time of the inspection.  No destructive testing or dismantling of building components is performed.

It is the goal of the inspection to put a homebuyer in a better position to make a buying decision.  Not all improvements will be identified during this inspection.  Unexpected repairs should still be anticipated.  The inspection should not be considered a guarantee or warranty of any kind.

Please refer to the pre-inspection contract for a full explanation of the scope of the inspection.

WEATHER CONDITIONS

Dry weather conditions prevailed at the time of the inspection.  The estimated outside temperature was 54 degrees F.  Occasional rain has been experienced in the days leading up to the inspection.

# Structural Components

## description of structural components

Foundation: 	(Poured Concrete  (Basement Configuration

Floor Structure: 	(Wood Joist

Wall Structure: 	(Wood Frame

Ceiling Structure: 	(Joist

Roof Structure: 	(Roof Joists  (Plywood Sheathing

## structural component observations

### recommendations / observations

- Monitor:  Common minor cracks were observed in the foundation walls of the house.  This implies that some structural movement of the building has occurred, as is typical of most houses.

- Improve:  Surface deterioration was observed on the interior of the exposed foundation walls.  This condition is common in many older homes and does not usually represent a serious structural concern.  In an effort to prevent long-term deterioration, it would be wise to consider parging all deteriorated areas.  Lot drainage improvements, as outlined in the “Exterior” section of this report are also recommended.

## limitations of structural component inspection

As prescribed in the pre-inspection contract, this is a visual inspection only.  Assessing the structural integrity of a building is beyond the scope of a typical home inspection.  A certified professional engineer is recommended where there are structural concerns about the building.  Inspection of structural components was limited by (but not restricted to) the following conditions:

- Structural components concealed behind finished surfaces could not be inspected.

- Only a representative sampling of visible structural components were inspected.

Please also refer to the pre-inspection contract for a detailed explanation of the scope of this inspection.

# Roofing System

## description of roofing System

Roof Covering: 	(Asphalt

Chimneys: 	(Masonry

Gutters and Downspouts: 	(Galvanized Steel  (Downspouts discharge below grade

Method of Inspection: 	(Walked on roof

## roofing observations

### recommendations / observations

- Improve:  Minor repairs to the roofing are recommended.  Damaged or missing roofing material should be repaired.  All roof penetrations should be examined and sealed as necessary.

- Improve:  The masonry chimney is in need of re-pointing (replacing the mortar between the bricks).

- Improve:  The gutters require cleaning.

## limitations of roofing inspection

As prescribed in the pre-inspection contract, this is a visual inspection only.  Roofing life expectancies can vary depending on several factors.  Any estimates of remaining life are approximations only.  This assessment of the roof does not preclude the possibility of leakage.  Leakage can develop at any time and may depend on rain intensity, wind direction, ice build up, etc.  The inspection of the roofing system was limited by (but not restricted to) the following conditions:

- The entire underside of the roof sheathing is not inspected for evidence of leakage.

- Interior finishes may disguise evidence of prior leakage.

Please also refer to the pre-inspection contract for a detailed explanation of the scope of this inspection.

# Exterior Components

## description of exterior

Wall Cladding: 	(Wood Siding

Soffit and Fascia: 	(Wood

Window/Door Frames and Trim: 	(Wood  (Vinyl

Driveways: 	(Concrete

Walkways and Patios: 	(Concrete

Porches, Decks, and Steps: 	(Concrete  (Wood

Overhead Garage Door(s): 	(Steel  (Automatic Opener

Lot Grading: 	(Level Grade

Fencing: 	(Wood

## exterior observations

### recommendations / observations

- Safety Issue:  The garage door opener did not automatically reverse under resistance to closing.  There is a serious risk of injury, particularly to children, under this condition.  Improvement may be as simple as adjusting the sensitivity control on the opener.  This should be dealt with immediately.

- Improve:  Tree branches should be trimmed away from the house.

- Improve:  The window frames should be caulked and painted.

- Improve:  As is very typical, the basement windows have been neglected.  They should be repaired or replaced as needed.  Wood/soil contact should be avoided.

## limitations of exterior inspection

As prescribed in the pre-inspection contract, this is a visual inspection only.  The inspection of the exterior was limited by (but not restricted to) the following conditions:

- A representative sample of exterior components was inspected.

- The inspection does not include an assessment of geological conditions and/or site stability.

Please also refer to the pre-inspection contract for a detailed explanation of the scope of this inspection.

# Electrical System

## description of ELECTRICAL System

Size of Electrical Service: 	(120/240 Volt Main Service – 200 Amp / Copper Supply

Service Entrance Wires: 	(Overhead

Service Ground: 	(Copper

Main Distribution Panel: 	(Breakers

Distribution Wiring: 	(Copper

Receptacles: 	(Grounded

Ground Fault Circuit Interrupters: 	(Bathroom(s)  (Exterior  (Kitchen  (Garage

## Electrical observations

### recommendations / observations

- Improve:  Wiring exposed on interior finishes (loose wires in laundry room) should be relocated or protected by a rigid conduit.

- Improve:  Missing outlet cover plates should be replaced (front bedroom & bathroom).

- Improve:  Recessed lights should be fitted with bulbs suitable to this application (flood or spot lights).  Otherwise, there is a risk of overheating.

## limitations of electrical inspection

As prescribed in the pre-inspection contract, this is a visual inspection only.  The inspection does not include low voltage systems, telephone wiring, intercoms, alarm systems, TV cable, timers or smoke detectors.  The inspection of the electrical system was limited by (but not restricted to) the following conditions:

- Electrical components concealed behind finished surfaces could not be inspected.

- Only a representative sampling of outlets and light fixtures were tested.

Please also refer to the pre-inspection contract for a detailed explanation of the scope of this inspection.

# Heating System

## description of heating System

Primary Energy Source: 	(Gas

Heating System Type: 	(Forced Air

Heat Distribution Methods: 	(Ductwork

## Heating observations

### recommendations / observations

- Improve:  The heating system requires cleaning and servicing.

- Improve:  The chimney serving the gas fired heating system does not appear to be lined.  Chimney liners are typically required.

## limitations of heating inspection

As prescribed in the pre-inspection contract, this is a visual inspection only.  The inspection of the heating system is general and not technically exhaustive.  A detailed evaluation of the furnace heat exchanger is beyond the scope of this inspection.  The inspection was limited by (but not restricted to) the following conditions:

- The adequacy of heat distribution is difficult to determine during a one-time visit to a home.

Please also refer to the pre-inspection contract for a detailed explanation of the scope of this inspection.

# Cooling / Heat Pump System

## description of Cooling / heat pump system

Energy Source: 	(Electricity

System Type: 	(Air Cooled Central Air Conditioning

## system observations

### recommendations / observations

- Improve:  The outdoor unit of the air conditioning system is out of level.  This should be improved.

## limitations of cooling / heat pump system inspection

As prescribed in the pre-inspection contract, this is a visual inspection only.  Air conditioning and heat pump systems, like most mechanical components, can fail at any time.  The inspection of the cooling system was limited by (but not restricted to) the following conditions:

- Window mounted air conditioning units are not inspected.

- The adequacy of distribution of cool air within the home is difficult to determine during a one-time inspection.

Please also refer to the pre-inspection contract for a detailed explanation of the scope of this inspection.

# Insulation / Ventilation

## description of Insulation / Ventilation

Attic Insulation: 	(R30 Fiberglass in Main Attic

Roof Ventilation: 	(Roof Vents  (Fascia Vents

Exhaust Fan/vent Locations: 	(Bathroom  (Kitchen

## insulation / ventilation observations

### recommendations / Energy saving Suggestions

- Improve:  Insulation should be evened out above the kitchen area (appears that electrical work has been performed in this area and insulation was shifted).

## limitations of insulation / ventilation inspection

As prescribed in the pre-inspection contract, this is a visual inspection only.  The inspection of insulation and ventilation was limited by (but not restricted to) the following conditions:

- Insulation/ventilation type and levels in concealed areas cannot be determined.  No destructive tests are performed.

- Potentially hazardous materials such as Asbestos and Urea Formaldehyde Foam Insulation (UFFI) cannot be positively identified without a detailed inspection and laboratory analysis.  This is beyond the scope of the inspection.

- An analysis of indoor air quality is beyond the scope of this inspection.

- Any estimates of insulation R-values or depths are rough average values.

Please also refer to the pre-inspection contract for a detailed explanation of the scope of this inspection.

# Plumbing System

## description of plumbing system

Service Pipe to House: 	(Copper

Main Valve Location: 	(Laundry Room

Supply Piping: 	(Copper

Drain / Waste / Vent Piping: 	(Plastic

Water Heater: 	(Gas  (Approximate Capacity (in gallons): 50

## plumbing observations

### recommendations / observations

- Improve:  Water heaters should be anchored or strapped to resist movement during possible earthquake conditions.

- Monitor:  The bathroom sink was observed to drain slowly, suggesting that an obstruction may exist. Try liquid drain cleaner as a first resort.

- Improve:  The toilet runs on after flushing.  Improvement to the tank mechanism is likely to be needed.

## limitations of plumbing inspection

As prescribed in the pre-inspection contract, this is a visual inspection only.  The inspection of the plumbing system was limited by (but not restricted to) the following conditions:

- Portions of the plumbing system concealed by finishes and/or storage (below sinks, etc.), below the structure, and beneath the yard were not inspected.

- Water quality is not tested.  The effect of lead content in solder and or supply lines is beyond the scope of the inspection.

- In older homes, it is wise to have the sewer line scoped for possible breaks in the line. Consult with a licensed plumbing contractor.

Please also refer to the pre-inspection contract for a detailed explanation of the scope of this inspection.

# Interior Components

## description of Interior

Wall and Ceiling Finishes: 	(Drywall/Plaster

Floor Surfaces: 	(Carpet  (Vinyl/Resilient  (Wood

Doors: 	(Wood  (Sliding Glass

Fireplaces: 	(Masonry Firebox

## Interior observations

### recommendations / observations

- Monitor:  Evidence of patching was detected in the living room ceiling (below the upper master bathroom). This area should be monitored.

- Improve:  The door to the garage should be trimmed or adjusted as necessary to work properly.

- Improve:  Loose stairway handrails should be better secured.

- Improve:  The fireplace damper is stuck in the open position and requires repair.

- Monitor:  Carbon monoxide is a colorless, odorless gas that can result from a faulty fuel burning furnace, range, water heater, space heater or wood stove.  Proper maintenance of these appliances is the best way to reduce the risk of carbon monoxide poisoning. For more information, consult the Consumer Product Safety Commission at 1-800-638-2772 (C.P.S.C.) for further guidance.  It would be wise to consider the installation of carbon monoxide detectors within the home.

## limitations of Interior inspection

As prescribed in the pre-inspection contract, this is a visual inspection only.  Assessing the quality and condition of interior finishes is highly subjective.  Issues such as cleanliness, cosmetic flaws, quality of materials, architectural appeal and color are outside the scope of this inspection.  Comments will be general, except where functional concerns exist.  No comment is offered on the extent of cosmetic repairs that may be needed after removal of existing wall hangings and furniture.  The inspection of the interior was limited by (but not restricted to) the following conditions:

- Furniture, storage, appliances and/or wall hangings may have restricted the inspection of the interior.

- Discovery or testing for mold is not within the scope of this inspection. If you have any concerns regarding mold, consult with a mold specialist.

Please also refer to the pre-inspection contract for a detailed explanation of the scope of this inspection.

# Appliances

## description of Appliances

(Gas Range  (Microwave Oven  (Dishwasher  (Waste Disposer  (240 Volt Circuit for Dryer  (Dryer Vented to Building Exterior  (120 Volt Circuit for Washer  (Hot and Cold Water Supply for Washer  (Waste Standpipe for Washer  (Door Bell  (Smoke Detectors

## Appliance observations

### recommendations / observations

- Improve:  The front right burner on the gas range is inoperative. This should be repaired immediately.

- Improve:  The kitchen exhaust hood fan is noisy. Consider repair or replacement.

- Improve:  The doorbell is inoperative.

## limitations of Appliance inspection

As prescribed in the pre-inspection contract, this is a visual inspection only.  Appliances are tested by turning them on for a short period of time.   It is strongly recommended that a Homeowner’s Warranty or service contract be purchased to cover the operation of appliances.  It is further recommended that appliances be tested during any scheduled pre-closing walk through.  Like any mechanical device, appliances can malfunction at any time (including the day after taking possession of the house).  The inspection of the appliances was limited by (but not restricted to) the following conditions:

- Thermostats, timers and other specialized features and controls are not tested.

- The effectiveness, efficiency and overall performance of appliances is outside the scope of this inspection.

Please also refer to the pre-inspection contract for a detailed explanation of the scope of this inspection.